## Slide 1: Gate Three - Adoption Laminar Flow Restrictor (LFR)
Patrick Moore
EE Products
June 2018

## Slide 2: Executive Summary
  Market Problem Statement
    The Office of Statewide Health Planning and Development (OSHPD) regulations in the state of California specifically bans the use of water restricting aerators in the health care industry due to the aerator’s flow control methods and components.
    The lack of aerators allows for increased water usage and a need to heat water more often
  Project Description
    Adopt So Cal Gas Laminar Flow Restrictors (LFR) workpaper WPSCGNRWH150827A
    OSHPD approved LFRs act similar to aerators by restricting the flow of water
    A reduced flow rate over a similar operating time would result in a reduction of hot water usage, therefore reducing the amount of natural gas used.
  Strategic Fit
    Saves water (See Appendix B)
    Saves natural gas (around 18 Therms/yr per sink)
    Deemed is a more cost effective alternative than Custom for this measure: $0.26/Therm to administer based on (Rebate + Admin)/(annual Therm savings)
  Request
    Approval to adopt So Cal Gas Laminar Flow Restrictors (LFR) workpaper

## Slide 3: Supporting Questions
  Cost and Approval Status
    Deemed budget to be planned for 2019: $23,400; 2020: $46,800
    Project timeline:
      Workpaper Adopted: June 2018
      CPUC Workpaper approved: July 2018
      Product Launch: August 2018
  Key Metrics
    TRC ~ 4.61
    Savings of 96,660 Therms/yr
  Stakeholders Impacted
    There are currently no regulations requiring this product.
  Major Risks
    Short payback may cause product to be considered a “Free-rider” (Note that this Workpaper has been in use with So Cal Gas since 2015)
  Risk Mitigation
    The product will be evaluated on an annual basis to examine uptake. If uptake reaches 80% of the market or adoption occurs in an uncommonly high rate, product will be pulled due to market transformation.

## Slide 4: Product Overview
Product Description: | Laminar Flow Restrictors (LFRs) for health care facilities (0.5 GPM-2.2 GPM flow rates) that are installed at the outlet of faucet spouts to reduce flow rate and thus water consumption (See Appendix A)
Market Overview: | ISP is to have no water restricting device on hospital faucets LFRs are a relatively new technology and are not currently represented in DEER
Manufacturers: | Only LFR models labeled as “Vandal Proof” or are not removable without a proprietary tool are considered for the rebate, with the exception of dialysis and scrub sink locations. There are currently 37 “Vandal Proof” LFRs in the appropriate size options available for purchase.
Channels Utilized: | Deemed
Target Customer: | Hospitals (large regional or local) Emergency rooms In-patient and outpatient facilities and medical office buildings connected to or free standing from main hospitals Doctor’s offices (e.g. general practitioners, pediatricians, optometrists, chiropractors, etc.)

## Slide 5: Key Metrics for EE – Sample Product
Value Proposition for customer
Cost Effectiveness
Market Information
Product Budget
Per Year Bill Savings per unit | $ 18
Lifetime Bill Savings per unit | $ 360
Upfront Customer Cost | $ 7.27
Payback w/Incentive | 1/2 yr
Payback w/o Incentive | 1/5 yr
Saves up to 5,425 Galons of water per year
Saves around 18 Therms/yr per sink
Assume Rebate is 55% of IMC (Appendix C) = $4.00
 | Units | Energy Savings
Realistic Achievable Market Potential | 21,480 | 386,630 Therms
Budget Constraint RAP (5% Participation rate) | 5,370 | 96,660 Therms
 | Most Probable Scenario* | Worst Case Scenario
TRC | 5.88 | 4.61
PAC | 7.47 | 7.47
Funding Source: Program Budget
Planned For 2019
Incremental Budget:$50,000
Customer-Based
Internal
*Admin does not include Marketing or Contracts
Assumptions: Commercial Deemed
EUL: 20 yrs
RUL: 6.67 yrs
NTG: 0.6
Budget | 2019 | 2020 | 2021
Forecast Quantity | 5,000 | 10,000 | 10,000
Forecast Incentive ($) | 20,000 | 40,000 | 40,000
Admin ($) | 3,400 | 6,800 | 6,800
Marketing ($) | Roll into regular outreach campaigns |  | 
See Appendix D for Estimated Market Details

## Slide 6: Core Team and Approvals to Date
Department |  | Core Team Member(s) | Discussed w/ Core Team Member (y/n) | Approver for Email, Resource, & Relevant Brief Section (Manager or above)
As Relevant to Project |  |  |  | 
 | Application Management/ Verification | Brandy Taylor | N | Patrick Hodgson
 | Codes and Standards |  |  | 
 | Custom Solutions Delivery | Matt Coffman Vince DiCicco | Y | Marcela Fox
 | Deemed Product Support | Steve Fok | Y | Henry Liu
 | EM&V | TBD | N | Lucy Morris
 | Policy | TBD | Y | Halley Fitzpatrick
 | Product Management | Patrick Moore | Y | Mananya Chansanchai
 | Portfolio Management | Erika Nagy | Y | Harry Charalambides
 | Solutions Marketing | Trish Berg / Erik Olsen | N | Jamie Chesler
 | Technology Enablement |  | N | Enida Reyes

## Slide 7: Program Appendix
Additional Material Required for Program Launch

## Slide 8: Appendix A: LFR vs Aerator Comparison
LFRs | Aerators
“Laminar” refers to a stream that flows in parallel layers with no disruption between them Approved for health care use because of their hygienic advantage: aerosol generation is reduced to a minimum due to the lack of air intake Water restriction is achieved by using small nozzles (straightening vanes) that are shaped to keep turbulence from forming, preventing air from entering the flow Flow is clear and transparent | Use the Venturi effect to introduce air into the water stream Banned in health care environments, but commonly used in residential and other commercial applications Restrict water by using screens to introduce air bubbles into the water stream which may allow airborne bacteria to become waterborne Flow has a white opacity and a soft feel

## Slide 9: Appendix B: Water Savings
Water Savings | Units | 2.2 GPM | 1.5 GPM | 1.0 GMP | 0.5 GPM
 | gal/yr | 1,233 | 2,959 | 4,192 | 5,425
The savings calculation approach for this measure compares the energy consumption of the domestic hot water (DHW) system of the existing condition (faucets without LFRs) with the proposed condition (faucets with LFRs). This analysis is based on the first law of thermodynamics (conservation of energy). The installation of LFRs causes a change in the mass flow rate of water and thus ultimately affects the thermal load of the system.

## Slide 10: Appendix C: Incremental Measure Cost
Installation Type | Incremental Measure Cost | Full Measure Cost | 
 |  | 1st Baseline | 2nd Baseline
REA, Direct Install | $7.27/fixture + $7/fixture = $14.27 per fixture | $14.27 per fixture | N/A
REA, Downstream Prescriptive Rebate | $7.27/fixture + $0/fixture = $7.27 per fixture | $7.27 per fixture | N/A

## Slide 11: Appendix D: PG&E Estimated Market
Type | NAICS | NAICS Count (# of facilities) | Est. # of Sinks | Avg Therm savings (18 Therms/yr per sink) | 5% market Therms | 20% market Therms | 5% market Units | 20% market Units
Outpatient Buildings | 621420, 621498, 622210 | 732 | 11,462 | 206,311 | 10,316 | 41,262 | 573 | 2,292
Nursing Care Facilities | 621399, 621610, 623110 | 1,504 | 50,009 | 900,158 | 45,008 | 180,032 | 2,500 | 10,002
Hospitals | 621493, 622110, 622310, 623210 | 378 | 45,927 | 826,686 | 41,334 | 165,337 | 2,296 | 9,185
Total |  | 2,614 | 107,397 | 1,933,154 | 96,658 | 386,631 | 5,370 | 21,479