## Slide 1: DEER2026 Update Resolution E-5350
Webinar November 25, 2024
Ex Ante Review Team

## Slide 2: Webinar Participation
All attendees are muted on entry
How to participate in this webinar:
  Please use the chat box to submit questions
  We will read and respond to questions at the end of each section
During the wrap-up Q&A session, use the “raise hand” option in Webex:
  Use the button to raise your hand and the host will call on you
  Please state your name and affiliation when you ask your question
  Please turn off the raised hand after your question
  This Webinar is being recorded. Participation implies permission to be recorded.
Slides are posted to the Public Document Area
  https://pda.energydataweb.com/#!/ (Search using DEER2026)

## Slide 3: Welcome
DEER and Measure Package Team leads
  CPUC: Peter Biermayer
  DNV: Jennifer McWilliams, Rachel Murray, Dan Pidgeon, and Cameron Tuttle
2026 DEER update cycle highlights
  Continued DEER update cycle revisions due to Decision D.21-05-031
  Transition of prototype models from eQUEST/DOE2 to EnergyPlus
  Calls for future research
Goal of this Webinar: To provide an opportunity for interactive Q&A of the DEER Update Resolution prior to finalizing Dec. 17, 2024

## Slide 4: DEER2026 Update Implementation Schedule
Milestone | Date
Draft Resolution posted to CPUC website | November 14, 2024
Draft Resolution sent to service list R13-11-005 | November 14, 2024
Draft Resolution webinar | November 25, 2024
Stakeholder comments* due | December 4, 2024
Final Resolution voted out | December 19, 2024
* Refer to the tariff comment letter sent out to the service list

## Slide 5: DEER Update Presentation Schedule
Introduction (10 min) 9:30 a.m. – 9:40 a.m.
Management of DEER Processes (15 min) 9:40 a.m. – 10:10 a.m.
Research for PY 2028-29 (10 min) 10:10 a.m. – 10:15 a.m.
Research Based Guidance (10 min) 10:15 a.m. – 10:25 a.m.
Measure Adoption (5 min) 10:25 a.m. – 10:30 a.m.
Wrap up and Final Q&A (15 min) 10:30 a.m. – 10:45 a.m.

## Slide 6: Management of DEER Processes
9:40 a.m. – 10:10 a.m.

## Slide 7: Updates to eTRM
California’s eTRM is the Official Source of California Energy Efficiency Measure Data and the sole source for energy efficiency measure package development, submittal, review, and publishing.
Funding
Source Code/Documentation using Git platform
Measure Lifecycle Management table in DEER
Assess Enabling Filtering on CPUC Support Tables
Effective: 2024-2028

## Slide 8: eTRM Structural Change to Data Tables
DEER’s Source Status table is no longer maintained Effective: 2024
Fuel Sub ID fieldname/table is replaced with Fuel ID fieldname/table Effective: 2026
New fields: Effective: 2028
    Net lifecycle refrigerant leakage emissions
    Refrigerant type for measure, standard practice, and existing equipment cases
    In addition to whole building energy consumption fields, provide end-use energy consumption fields for each case
Retire DEER Measure ID Effective: 2028
Effective: 2024-2028

## Slide 9: DEER System and Measure Package Updates: Refrigerant leakage impacts and costs
Determined using RACC-FSC_v3.0/3.1* workbooks:
Measure Package Update Type | ACC Version**
New offering(s) added to existing approved measure package for PY2024-2025 | ACC2022 values shall be used in RACC-FSC for new offering permutations, only
Mid-cycle updates to existing approved measure packages for PY2025 | ACC2022 values shall be used for all permutations
Measure package updates for PY2026 | ACC2024 values shall be used for all permutations
New measure packages for PY2026 | 
* RACC-FSC_v3.1 calculations are identical to those in RACC-FSC_v3.0; the key difference is that v3.1 enables differentiation between EUL_ID versions that
have different EUL values (e.g., for the HV-ResHP EUL_ID, DEER2014 has an EUL of 15 years whereas DEER2025/DEER2026 has an EUL of 23 years).
** The RACC-FSC_v3.0/3.1 workbooks allow users to select which Avoided Cost Calculator (ACC) version is to be used.
Effective: 2024-2026

## Slide 10: DEER System and Measure Package Updates: RACC-FSC_v3.0/v3.1 workbooks
Measure Type | 2 RACC worksheet | 3 FSC worksheet
Efficiency rating differs between the measure, standard practice, and/or existing equipment cases (i.e., refrigerant type and amount is the same between the cases) | Not required | Not required
Type of refrigerant differs between or changes for the measure, standard practice, and/or existing equipment cases | X | Completion required only for fuel-substitution measures
Amount (charge) of refrigerant differs between or changes for measure, standard practice, and/or existing equipment cases | X | 
Claiming avoided emissions when refrigerant in existing equipment is recovered and documentation provided* | X | 
Fuel substitution measure without refrigerant (e.g., induction range) | X** | X
* Although the RACC spreadsheet has the functionality to claim credit for refrigerant recovery, it is not currently sanctioned by the CPUC.
** The “2 RACC” worksheet contains a dropdown menu that includes “No refrigerant” to indicate when equipment contains no refrigerant. The “2 RACC”
worksheet must be filled in prior to any use of the “3 FSC” worksheet.
Effective: 2024-2026

## Slide 11: DEER System and Measure Package Updates
Water-Energy Nexus (WEN) Impacts long term solution is now implemented. The CET was updated to include a separate field for embedded water savings.
Lighting Baseline Updates. The standard practice baseline in measure packages will conform to the updated values in the Modified Lighting Calculator (MLC).
Effective: 2024-2026

## Slide 12: DEER System and Measure Package Updates
Definition of Incentive and Rebate. Per D.08-07-006:
The SPM [standard practice manual] defines the incentive (INC) term very narrowly as the type of incentive that can be treated as a transfer payment in the SPM TRC [Total Resource Cost] formulation. The definition of the INC term, as set forth in the SPM, is restricted to "dollar benefits" such as rebates or rate incentives (monthly bill credits) paid by the sponsoring utility to the customers participating in the program. Moreover, the SPM is very clear that the term "participant" refers to the customer participating in the program, and that this transfer incentive (INC) is one that is paid directly to the participating customer.
Deemed Measure Cost and Incentive Reporting. Measure level incentives (UnitDirectInstallLab, UnitDirectInstallMat, UnitEndUserRebate, UnitIncentiveToOthers) include only the portion of the incentive that reduces the customer cost of the measure.
Peak Load Definition has not changed. The peak demand window is still from 4 p.m. to 9 p.m.

## Slide 13: DEER System and Measure Package Updates
Vintage and Era Definitions are revised. Starting in PY2026, the recent and old building eras are removed, and the existing era represents all existing buildings.
DEER Prototype Models have transitioned from a DOE2-based system to EnergyPlus. The new system uses ModelKit to facilitate input file creation and running batch simulation models. PY2026 measure packages will use 2025 T-24 as the baseline.
Data Requirements outlined in Resolution E-5221 should continue to be listed in measure packages moving forward. SiteID is not a replacement for end use or customer tracking data for evaluation purposes.

## Slide 14: DEER 2028 Update and Measure Package Submission/Review Timeline
Description | Responsible Party | Due Date | Approval Date | Effective Date
Measure Package Update Schedule | PAs/ Stakeholders | 2025-08-01** | - | -
Measure Package Submittals | PAs | 2026-03-31 to CPUC | 2026-07-31+ | 2028-01-01*
Draft DEER2028 Update Resolution | CPUC | 2026-07-31 | - | -
DEER2028 Update Resolution | CPUC | - | 2026-10-30 | 2028-01-01*
* There may be exceptions when updates become effective mid-cycle.
** Draft for workflow scheduling. Updates to the schedule may be made if needed.
+ Per Draft Resolution release, adoption in Final Resolution

## Slide 15: DEER Mid-Cycle Adjustments to the Locked Ex-Ante Values
New measure packages and additions to measure packages may be submitted for CPUC staff review at any time during the biennial cycle
All error corrections will be handled on a case-by-case basis
Anticipated changes to codes and standards that occur off-cycle shall be planned for and may necessitate mid-cycle updates to measure packages.
Uncertain or unanticipated changes to codes and standards that occur off-cycle will require a revised measure package baseline and become effective 90 days after the measure package is approved

## Slide 16: Structural Changes - New DEER Tables
FuelID
  EE-Elec-Only
  Exempt
  Exempt-FuelSub-ToElec
  Exempt-NC-AllElec
  None
  NonExempt-FuelSub-ToGas
  NonExempt-EE-Gas-Ex
  NonExempt-EE-Gas-New
  NonExempt-EE-Gas-New-NoVEA
Retire FuelSub table (replaced by FuelID table)
BldgWts
  Building Type weights
  Building Vintage weights
  Building HVAC weights
  FS-rImputedDX weights (for use with RACC-FSC to impute cooling when the baseline residential space-conditioning equipment does not include cooling)
Effective: 2024-2026
Effective: 2026

## Slide 17: Structural Changes to DEER Tables
Locking Measure and Energy Impact Tables. Records will no longer be added to either the “Measure” table for the “EnergyImpact” Table. These values will be entirely held in eTRM.
New fields in TechType table:
  IsExempt
  HasElecAlt
  HasRefrigerant
  HasRefrigerantAlt
UsesElec
UsesGas
  Fields proposed for deletion in TechType table:
    NormUnit
    defEULCode
Effective: 2026
Effective: 2024
Effective: 2028

## Slide 18: Updates to DEER Support Tables: Tech Types
Effective: 2026
Many new TechTypes were created so that each TechType consists only of equipment that uses one type of primary fuel (e.g., Fryers was expired and replaced with Fryers-Electric and Fryers-Gas).
New fields in TechType table:
    IsExempt
    HasElecAlt
    HasRefrigerant
    HasRefrigerantAlt
  UsesElec
  UsesGas
Effective: 2024
  Fields proposed for deletion in TechType table:
    NormUnit
    defEULCode
Effective: 2028

## Slide 19: Updates to DEER Support Tables
The following NTG IDs are expired since they should no longer be used:
    All-Ltg-LED-WRR
    NonRes-Out-Ltg-LEDFixt
    Res-InCmn-Ltg-LEDFixt
    Res-OutCmn-Ltg-LEDFixt
Measure Impact Types are consolidated as follows:
    Cust-Gen
    Cust-NMEC-Pop
    Cust-NMEC-Site
    Cust-RCT
    Cust-SEM
    Deem
Effective: 2024
Effective: 2026

## Slide 20: Updates to DEER Support Tables: Delivery Types
Delivery Type | Formerly | Description of Delivery Type
Up-Manuf | UpDeemed | Incentivizes an energy-efficient technology through a program administrator partnership with the manufacturer
Mid-Distr |  | Incentivizes an energy-efficient technology through a program administrator partnership with the distributor
Mid-Retail |  | Incentivizes an energy-efficient technology through a program administrator partnership with the retailer
Down | DnDeemed and DnCust | Incentivizes an energy-efficient technology or service to a participating customer for them to install or have installed
DI | DnDeemDI and DnCustDI | Incentivizes the downstream delivery and/or installation of an energy efficient technology and/or service at a customer property by a program implementer-managed third-party contractor or trade professional. Program incentives are paid directly to the installation contractor or technology/service provider. (see guidance memo on CEDARS site for details)
C&S | None | Codes and Standards (C&S advocacy and related programs)
Effective: 2026

## Slide 21: Updates to DEER Support Tables
EULs were added or updated for some residential weatherization measures, residential fan controller, cold water measures, and commercial patio heaters. These updates were to support DEER2024 and mid-cycle updates.
Updates to Building Weights using 2022 Commercial End Use Study (CEUS)
New Gas Impact Profile IDs
    Annual-FuelSub-ToElec
    Winter-FuelSub-ToElec
    Summer-FuelSub-ToElec
  *Error correction. To become effective 2028
Effective: 2024 *2028
Effective: 2024
Effective: 2026

## Slide 22: Research for PY2028-29
10:10 a.m. – 10:15 a.m.

## Slide 23: Research to Improve Refrigerant Charge Values
Better understand refrigerant charge (lb./NormUnit) for HVAC systems and products sold in California.
Research Questions:
Does the amount of refrigerant charge increase proportionally to the Cap-Tons for air conditioning equipment for all sizes? Should these be binned?
Does the amount of refrigerant charge increase proportionally to the Cap-kBtuh for HVAC heat pump equipment? Should these be binned?
Does the amount of refrigerant charge vary by efficiency tier? And if so, by how much?
Does the amount of refrigerant charge vary by refrigerant? And if so, by how much?
Complete by December 2025 to inform the PY2028-29 cycle.

## Slide 24: SDG&E Research: Variable Refrigerant Flow (VRF) Heat Pump and AC Performance Curves
Parameter updates to high efficiency equipment
  Focus on commercial building HVAC equipment performance
  Initial Light Commercial Variable Speed Heat Pump Performance Map completed
FSEC-CR-1910-12 “Creating Performance Curves for Variable Refrigerant Flow Heat Pumps in EnergyPlus”
This update will inform the PY2028-29 cycle.

## Slide 25: CPUC Research: Improve Water Heater Measures
Future research to:
  Investigate availability of commercial hot water load profiles in 2019 Commerical End Use Study (CEUS)
  Develop additional activity-level water heating load shapes (e.g., gyms, laundromats)
  Investigate pathways to migrate commercial measures from DEER Water Heater Calculator to EnergyPlus
  Develop performance curves for different ambient conditions and refrigerant types
Complete by December 2025 to inform the PY2028-29 cycle.

## Slide 26: Research-based Guidance (EM&V and other studies)
10:15 a.m. – 10:25 a.m.

## Slide 27: Guidance from 2021 Custom Industrial, Agricultural, and Commercial (CIAC) Impact Evaluation Review
Effective Program Year: 2026. We direct the following:
Lighting applications should use area-specific hours of use (HOU) categories when the DEER building-specific hours of use are found to be inappropriate for a given site.
  Further—per D.12.05.015—PAs may conduct a study to develop HOUs if DEER values are neither available nor applicable
Deemed portions of custom projects are filed as separate deemed claims and clearly identified in the custom application.

## Slide 28: Guidance Based on Other Studies
One study completed by DNV and two conducted by the IOUs as directed by Resolution E-5221. We find from the three completed studies the following:
Group A Forward-Looking Research: Cross-Program Net-to-Gross Ratios for Hard-to-Reach Customers
  Study found no statistically significant evidence to support having different NTGRs for participants in either residential or commercial direct install programs. We direct that the default NTGRs for direct install programs are modified to 0.90 for residential programs and 0.70 for commercial ones.
High-SEER Heat Pump and AC Performance Curves
  Adopt recommendations for modeling variable compressor systems: use the MULTISPEED function in EnergyPlus, setting the number of compressor speeds to 4, and using no cycling losses for speeds 4, 3, and 2.
  Adopt recommended measure package requirements: 1) Require the OEM-recommended controls & thermostats. 2. Outdoor units must be considered capable of “variable capacity” performance. 3) If high efficiency AHU offerings are pursued, consider performance requirements such as an ECM or ≥3 fan speed settings.

## Slide 29: Guidance Based on Other Studies
One study completed by DNV and two conducted by the IOUs as directed by Resolution E-5221. We find from the three completed studies the following:
Boiler Compliance with Condensation of Exhaust Gases and Energy Efficiency
  Order measure package developers revise impacts estimates for condensing boilers:
    Retrofit applications the boilers are expected to operate in condensing mode less than 50% of the time
    Expectation for condensing operation in new construction applications should be greater than 90%
  Programs claiming condensing boiler measures must ensure the following conditions are met:
    The hot water return temperature must be below 130 °F and the supply hot-water temperatures should not exceed 140 °F.
    For retrofit projects (replacing boilers only), ensure the existing end use equipment (e.g., heating coils, radiators, etc.) and recommissioning is designed for these lower supply temperatures.

## Slide 30: Guidance from Review of 2023 & '24 EM&V Reports for PY2021 & '22 Deemed Measure Claims
PY21 Res Direct Install Program EM&V report
  Residential smart thermostat measure savings methodology reviewed, no changes to 2026 measure package
  Residential brushless fan motor replacement measure required an update the measures assumed existing power draw, correction the modeled equipment sizing
  Residential faucet aerator measure savings methodology revised with updated hot water usage rates, electric water heater saturation, and changes to fixture flow rate values based on new research or the best available data

## Slide 31: Guidance from Review of 2023 & '24 EM&V Reports for PY2021 & '22 Deemed Measure Claims
Net-to-gross ratio updates:

## Slide 32: Guidance from Residential Insulation EUL Study
Published December 2023, PDA link: CPUC Group A 2023 Residential Insulation EUL Study Final Report.pdf
EULs effective 1/1/2024
Measure | Existing EUL_ID, years | DEER2024 EUL_ID, years
Ceiling Insulation (SWBE006) | BS-CeilIns: 20.0 | BS-CeilIns: 30.0
Wall Insulation, both blown-in and non-blown-in insulation (SWBE007) | BS-BlowInIns: 20.0 BS-WallIns: 20.0 | BS-BlowInIns: 30.0 BS-WallIns: 30.0

## Slide 33: Guidance from 2023 Residential HVAC and Water Heating EUL Study
Published in April 2024, effective 1/1/2025
Residential central air conditioner also updated to 23 years

## Slide 34: Guidance from 2023 Commercial HVAC and Water Heating EUL Study
Published May 2024, effective 1/1/2025
Studied commercial heat pump and heat pump water heater technologies and fuel substitution baselines

## Slide 35: Measure Adoption
10:25 a.m. – 10:30 a.m.

## Slide 36: PY2025 and PY2026-27 Measure Adoption
Tables A.1 and A.2 in the Resolution list PY25 (mid-cycle) and PY26-27 measure packages respectively:
  Approved and published measure packages can be viewed on eTRM website
    https://www.caetrm.com/dashboard/
  The resolution will be on the CEDARS website when final
    https://cedars.cpuc.ca.gov/deer-resources/deer-versions/2026/

## Slide 37: Wrap Up and Final Q&A
10:30 a.m. – 10:45 a.m.

## Slide 38: How to Submit Comments re Resolution E-5350
All comments must be submitted to Energy Division by Dec. 4, 2024
Draft Resolution E-5350 located at Proposed Decisions and Resolutions for Public Comment Results. Posted on November 14, 2024.
Comments along with a certificate of service shall be sent via email to: edtariffunit@cpuc.ca.gov
Also, copies of the comments shall be submitted via email to: Peter.Biermayer@cpuc.ca.gov and Leanne.Hoadley@cpuc.ca.gov.

## Slide 39: Thank you for participating!