## Slide 1: DEER EnergyPlus Prototype System
DEER EnergyPlus Transition Webinar #4
Jennifer McWilliams, Amine Lazrak, Yitian Liang, DNV
Peter Biermayer, CPUC
13 December 2023

## Slide 2: Introduction
Please make sure you are on mute
For webinar technical difficulties:
  Send email to Peter Biermayer: Peter.Biermayer@cpuc.ca.gov
Q&A Process (audio/chat)
  Ask questions in two ways:
  1) Audio/Voice (please raise your hand during designated Question periods at the end of each section)
  2) Type your question in the chat at any time
PPT and Recording will be here:
https://cedars.sound-data.com/deer-resources/tools/energy-plus/

## Slide 3: Introduction – Links
Send future questions to DEERSupport@dnv.com
Github Repository link: https://github.com/sound-data/DEER-Prototypes-EnergyPlus
    Access the DEER prototypes
Non-residential model documentation: https://calbem-benchmarking.com/docs/building-energy-models/non-residential/
CA EE Contracts Public Documents Area link: https://pda.energydataweb.com/#!/
    Access the slides
    Leave feedback

## Slide 4: Agenda
01
02
03
04
06
05
Overview - 5 minutes
New prototype system - 20 minutes
Post-processing - 8 minutes
Measure development procedures - 15 minutes
Next steps and questions - 10 minutes
Introduction - 2 minutes

## Slide 5: Overview
This webinar will present the new DEER Prototype system replacing MASControl3 ©
Migration of residential and commercial prototypes to EnergyPlus is almost complete.
  Residential prototypes were migrated in 2022
  Residential results were updated for PY2024 measure packages
  Commercial prototypes are migrating in December 2023
  EnergyPlus will be used for simulated measure savings estimates in PY2026 measure packages and going forward
The GitHub repository system allows a transparent collaborative process to continuously improve the DEER Prototype models

## Slide 6: Questions

## Slide 7: Measure development procedures
  Stay current on all GitHub repository updates during measure development
  Make changes to add the measure
  Submit pull requests through GitHub
  Include MeasureVersionID in the pull request
  Pull requests will be approved by DNV
  Wait for final approval and branch merge before final simulations
  All measure input files must be contained in the GitHub repository
Measure development process for PAs and Measure Package developers

## Slide 8: Measure development procedures
Fill out Section 3: Modeled Measures of the Measure Characterization Template
Fill in the UEC Modeling Tool Summary
  Include DEER GitHub path name
Zip the measure folder containing all Modelkit files
  Include as a reference in the measure package
All measures input files must be contained in the GitHub repository
Measure package documentation for PAs and Measure Package developers
Statewide Measure Characterization Template
Section 3 for Modeled Measures
Unit Energy Consumption (UEC) Modeling Tool Summary Example

## Slide 9: Measure development procedures
Permutations versus Modelkit organization
eTRM
Measure
  Offering
    Permutation (difference between two cases)
GitHub
Measure
  Climate Zone
    Cohorts
    · Case (one simulation)
GitHub Structure | GitHub Commercial |  |  |  |  |  |  | 
folder | cohort file |  |  |  |  | case name |  | 
Climate Zone | Building type | Building HVAC | Building Vintage | Tech group | Tech type | Simulation Type | Sector | Technology ID
CZ01 | OfL | cDXGF | 1975 | SpaceHtg_eq | GasFurnace | Pre (or Std or Msr) | Com | dxAC-Com-Pkg-110to135kBTUh-EER10.1-1Spd
eTRM Permutations Structure | eTRM Permutations Structure |  | 
Offering ID | Building Type | Building Vintage | Building Location
A | OfL | 1985 | CZ01

## Slide 10: Measure development procedures
Hierarchy of simulation outputs:
Runs
  Climate1
    Cohort1: BldgType&System&Vintage&TechGroup_TechType
              Existing Baseline
              Standard Baseline
              Measure Offering1
              Measure Offering2
              Etc…...…
    Cohort2: DMo&rDXGF&New&SpaceHtg_eq_GasFurnace
              Standard Baseline
              Measure Offering1
              Measure Offering2
              Etc…...…
    Etc……..
  Climate2
  Etc…….

## Slide 11: Measure development procedures
Commercial |  |  |  | 
Building type | Building HVAC | Vintage | Tech group | Tech type
OfL | cDXGF | 1975 | SpaceHtg_eq | GasFurnace
Residential |  |  |  |  | 
Building type | # of floors | Building HVAC | Vintage | Tech group | Tech type
DMo | 0 | rDXGF | Ex | SpaceHtg_eq | GasFurnace
Cohort file naming structure (a cohort is a group of simulations)

## Slide 12: Measure development procedures
Residential and Commercial case name structure | 
Simulation Type | Technology ID
Msr | Res-GasFurnace-AFUE92-ECM
Std | dxAC-PTAC-7to15k-8.2-RQ
Pre | dxAC-Com-Pkg-110to135kBTUh-EER10.1-1Spd
Case naming structure (a case is one simulation)
The Technology table will live on CEDARS so all stakeholders can add new Tech IDs as required

## Slide 13: Questions

## Slide 14: New prototype system – EnergyPlus™
Free open-source whole building energy simulation program
DOE releases major updates twice annually
Large community of users, contributors and maintainers
Large number of successful applications for most building types and systems

## Slide 15: New prototype system – EnergyPlus™
Input files
*.idf, *.epw
Results: Output files
*.csv, *.html, etc.
EnergyPlus environment
An input data file (IDF) is a text file containing the data describing the building and HVAC system to be simulated.

## Slide 16: New prototype system – EnergyPlus™ and Modelkit
Free and open-source, cross-platform framework for parametric modeling
Integrates two concepts:
  Templates to combine static content with dynamic inputs (multiple EnergyPlus objects connected to each other to form an integral system or component).
  Scripting to automate the IDFs generation and thus automate the modeling process.
IDF with R-11
Results R-11
IDF with R-60
Results R-60
Modelkit by Big Ladder Software
Weather files
List of Parameters
Templates
Root files

## Slide 17: New prototype system – Modelkit climate file
Modelkit:
Creates a list of IDFs for all combinations of climates and cohorts and runs them in EnergyPlus.
Simulations that belong to the same cohort and climate zone will have the same parameter values except those dependent on the measure.
Each cohort of simulations will be run in all specified climates.
Simulations belonging to the same cohort will use the same prototype model.
climate.csv
EPW
Climate zone
Code file
cohorts.csv
Climate/vintage dependent parameters
Root file
cases/
cases/
cohort_name.csv
Processing block 2:
List of parameter values that depend on measures (e.g. SEER, lighting densities, etc.)
Processing block 1:
List of parameter values that are dependent on climate zone or vintage: e.g. Envelop parameters
Simulations outputs
EnergyPlus

## Slide 18: New prototype system – Modelkit climate file
Example: climate file references code file
deer-dmo-1972-1985.csv file
climate.csv file

## Slide 19: New prototype system – Modelkit cohorts file
Modelkit:
Creates a list of IDFs for all combinations of climates and cohorts and runs them in EnergyPlus.
Simulations that belong to the same cohort and climate zone will have the same parameter values except those dependent on the measure.
Each cohort of simulations will be run in all specified climates.
Simulations belonging to the same cohort will use the same prototype model.
climate.csv
EPW
Climate zone
Code file
cohorts.csv
Climate/vintage dependent parameters
Root file
cases/
cases/
cohort_name.csv
Processing block 2:
List of parameter values that depend on measures (e.g. SEER, lighting densities, etc.)
Processing block 1:
List of parameter values that are dependent on climate zone or vintage: e.g. Envelop parameters
Simulations outputs
EnergyPlus

## Slide 20: New prototype system – Modelkit cohorts file
Example: step through simulation of each cohort file
cohorts.csv file
The simulation steps through the entire cohorts.csv file for every row in the climates.csv file.

## Slide 21: New prototype system – Modelkit cohorts file
cohorts.csv file
climate.csv file
Example: cohort file defines weather dependent or vintage dependent parameters

## Slide 22: New prototype system – Modelkit cases folder
Modelkit:
Creates a list of IDFs for all combinations of climates and cohorts and runs them in EnergyPlus.
Simulations that belong to the same cohort and climate zone will have the same parameter values except those dependent on the measure.
Each cohort of simulations will be run in all specified climates.
Simulations belonging to the same cohort will use the same prototype model.
climate.csv
EPW
Climate zone
Code file
cohorts.csv
Climate/vintage dependent parameters
Root file
cases/
cases/
cohort_name.csv
Processing block 2:
List of parameter values that depend on measures (e.g. SEER, lighting densities, etc.)
Processing block 1:
List of parameter values that are dependent on climate zone or vintage: e.g. Envelop parameters
Simulations outputs
EnergyPlus

## Slide 23: New prototype system – Modelkit cases folder
Example: cohort files that define cases are stored in the cases folder.
4 cohorts, each have a few cases: baselines and offerings

## Slide 24: New prototype system – Modelkit cases and cohort relationship
cases/ directory contains cohort CSVs that define parameter values that change for the baseline(s) and each measure offering.
  cohorts.csv determines the root file to use for each cohort and inserts weather dependent or vintage dependent parameters.

## Slide 25: New prototype system – How to use Modelkit
Install the following tools:
Modeling tools: EnergyPlus and Modelkit
Post processing tools: Python and a database management software
Version control tools: Git and an optional GUI if needed such as GitHub Desktop
Clone the remote project repository on GitHub
Home directory:

## Slide 26: New prototype system – Modelkit folders
codes contains T24 code files per year.
prototypes contains template root files per building type.
scripts contains Python and SQL programs to postprocess simulations’ outputs.
templates contains auxiliary templates.
weather contains weather files.
commercial measures and residential measures contain measures set up and parameters definition.

## Slide 27: New prototype system – Run simulations
Navigate to the measure folder and use the command “modelkit rake” to run specific group of measures

## Slide 28: New prototype system - Results
Results
  EnergyPlus Input files and hourly outputs
  Summary results

## Slide 29: Questions

## Slide 30: Post-processing - Overview
Output from ModelKit E+
Data Format Transformation pre-SQL process
PostgreSQL process impact calculation + weights
DEER database impacts
QC workbooks

## Slide 31: Post-processing - PostgreSQL scripts revisited
A series of PostgreSQL queries, applied in sequence
Resulting table becomes the measure impact savings records for the DEER database.
Similar to previous MC3 post-processes, updated with some modifications
Simulation outputs (used to come from MASControl3)
DEER measure impacts
SQL Scripts do the following:
combine 1-story and 2-story data for Single Family prototype (for Residential results only. Skipped for Commercial)
calculate kWh, therm and peak kW impacts (deltas)
apply HVAC weights / BldgType weights
round digits
(sim_annual.csv, sfm_annual.csv, current_msr_mat.csv, sim_hourly_wb.csv, sfm_hourly_wb.csv, etc..)
We need this format first..

## Slide 32: Post-processing - Python transformation before SQL
results-summary.csv
sim_annual.csv
sfm_annual.csv
current_msr_mat.csv
Output model IDFs, hourly consumptions, summary tables, etc.
sim_hourly_wb.csv
sfm_hourly_wb.csv
(EU tables as well, but work in progress)
Three BldgType specific scripts transform the data format of the Modelkit/E+ outputs to feed the postgreSQL scripts that produce the measure impacts.
Take individual hourly consumptions, rearrange into the 365x24 format sim_hourly / sfm_hourly
Take results-summary.csv rearrange into sim_annual / sfm_annual, apply correct normalizing units
Take all available info and create Measure-TechID relationship table (current_msr_mat)

## Slide 33: Questions

## Slide 34: Next Steps
December 2023 – Commercial prototypes will be added to the DEER Prototype system
Spring 2024 – Airflow Network will be added to the residential prototypes
Review and approve stakeholder updates to building prototype models and energy efficiency measures
Continue to work with CalBEM to update prototypes

## Slide 35: Questions

## Slide 36: DEER EnergyPlus Prototype System
DEER EnergyPlus Transition Webinar #4
Send future questions to DEERSupport@dnv.com
Jennifer.McWilliams@dnv.com
Peter.Biermayer@cpuc.ca.gov

## Slide 37: Reference Slides

## Slide 38: Introduction – Links
Github Repository link: https://github.com/sound-data/DEER-Prototypes-EnergyPlus
    Access the DEER prototypes
Non-residential model documentation: https://calbem-benchmarking.com/docs/building-energy-models/non-residential/
CEDARS link: https://cedars.sound-data.com/deer-resources/tools/energy-plus/
    Access the slides
    Calibration report
CA EE Contracts Public Documents Area link: https://pda.energydataweb.com/#!/
    Access the slides
    Leave feedback
Notes: You will need to set up a free github account. The github platform was chosen to increase transparency and stakeholder involvement.
Beyond today’s slides, there will also be a user guide located on CEDARS.
Slides will be posted (CEDARS and the PDA)
We will allow feedback on the pda, and we will review the comments but will not formally respond to comments

## Slide 39: New prototype system – GitHub
The remote repository can be accessed on sound-data/EnergyPlus (github.com)
Notes: This to explain where to find the repository.

## Slide 40: New prototype system – GitHub
Repository cloning example using GitHub Desktop (instructions available in the README.md file)
Notes: This to explain how to clone the repository.

## Slide 41: New prototype system – GitHub
Repository cloning example using GitHub Desktop (instructions available in the README.md file)
Notes: This to explain how to clone the repository.

## Slide 42: New prototype system – GitHub
Users bug fix and new measures addition
  Fork the remote repository
  Make changes on your local repository
  Submit a pull request
Notes: Explains how to submit a pull request
We will provide a template and instructions as well.