## Slide 1: DEER EnergyPlus Prototype System
DEER EnergyPlus Transition Webinar #3
Jennifer McWilliams
19 December 2022
Notes: Hi, I’m Jennnifer McWilliams from DNV and I’ll be presenting today with my colleagues Amine Lazrak and Yitian Liang on the new system that we’ve developed to house the DEER EnergyPlus Prototypes.

## Slide 2: Agenda
01
02
03
04
06
05
Overview - 7 minutes
New tools - 7 minutes
New prototype system - 7 minutes
Post-processing - 7 minutes
Github - 10 minutes
07
Updates to Calibration Memo - 10 minutes
Next steps and questions - 10 minutes
08
Introduction - 2 minutes
Notes: This is our agenda for today. After the introduction and Overview we will be diving into the details of how to use these new tools. Feel free to ask questions as we go along since we want to make sure that everyone understands the content we’re showing today. Don’t be shy, if you have a question, it’s likely that others have the same question.

## Slide 3: Links
Github Repository link: https://github.com/sound-data/DEER-Prototypes-EnergyPlus
    Access the DEER prototypes
CEDARS link: https://cedars.sound-data.com/deer-resources/tools/energy-plus/
    Access the slides
    Calibration report
CA EE Contracts Public Documents Area link: https://pda.energydataweb.com/#!/
    Access the slides
    Leave feedback
Notes: You will need to set up a free github account. The github platform was chosen to increase transparency and stakeholder involvement.
Beyond today’s slides, there will also be a user guide located on CEDARS.
Slides will be posted (CEDARS and the PDA)
We will allow feedback on the pda, and we will review the comments but will not formally respond to comments

## Slide 4: Overview
This webinar will present the new DEER Prototype system replacing MASControl3 ©
Migration of residential prototypes to EnergyPlus is complete for residential measures.
  Residential model results were updated
  New weather file, CZ 2022, was used for the simulations
  Measure simulation unit energy savings values were posted to DEER and are incorporated in new PY2024 measure packages
The calibration memo has been revised and final version posted on CEDARS
  https://cedars.sound-data.com/deer-resources/tools/energy-plus/
  The models were re-calibrated in response to public comments on the draft calibration memo

## Slide 5: New tools - EnergyPlus™
Free open-source whole building energy simulation program
DOE releases major updates twice annually
Large community of users, contributors and maintainers
Large number of successful applications for most building types

## Slide 6: New tools - EnergyPlus™
Input files
*.idf, *.epw
Output files
*.csv, *.html, etc.
EnergyPlus environment
An input data file (IDF) is a text file containing the data describing the building and HVAC system to be simulated.
Notes: We use one hour timesteps for the DEER simulations.
The EPW input is the weather file

## Slide 7: New tools - EnergyPlus™
Example of an EnergyPlus object (Fan) and how it is connected to objects (i.e. models) representing other building systems

## Slide 8: New tools - Modelkit
Free and open-source, cross-platform framework for parametric modeling
Integrates two concepts:
  Templates to combine static content with dynamic inputs (usually contains multiple EnergyPlus objects connected to each other).
  Scripting to automate the process of modeling
Input file R11
Output file R11
Input file R60
Output file R60
Modelkit
Weather files
List of Parameters
Templates
Root files
Notes: Root file is parameterized .idf files that takes the list of parameters, creating a different input file with each one.
Case files and code files are two types of files that contain lists of parameters.
Modelkit connects things together

## Slide 9: New tools – Modelkit – Root File
Example of how the EnergyPlus model can be parametrized within Modelkit.
Non-parametrized furnace model (EnergyPlus IDF)

## Slide 10: New tools – Modelkit – Root File
Example of how the EnergyPlus model can be parametrized within Modelkit.
Parametrized furnace model (Modelkit root file)

## Slide 11: New tools – Modelkit – Root File
All the parameters should be defined within the root file according to the Modelkit syntax.

## Slide 12: New tools - Modelkit
Ruby scripting
Example showing how the Modelkit scripting feature can be leveraged for model development and automation.
Predefined duct
template
These commands in the root file will insert in the IDF
all objects defining the ducts model in each of the zones
that were defined in the list ‘all_zones’

## Slide 13: New prototype system
Install the following tools:
EnergyPlus V9.5 and Modelkit
Python and a database management software
Git and an optional GUI for Git such as GitHub Desktop
Clone the remote project repository on GitHub
Home directory:

## Slide 14: New prototype system
Clone the remote project repository on GitHub
  Group of measures directory:

## Slide 15: New prototype system
Clone the remote project repository on GitHub
    cases: folder containing a csv file with lists of parameters’ values defining each measure. These parameters are also defined in the root file.
    climates.csv: a csv file with a list of weather files names.
    cohort.csv: a csv file indicating which root file to use for each defined case

## Slide 16: New prototype system
Install the following tools:
EnergyPlus V9.5 and Modelkit
Python and a database management software
Git and an optional GUI for Git such as GitHub Desktop
Clone the remote project repository on GitHub
Home directory:

## Slide 17: New prototype system
Run specific existing group of measures
  Open cmd on one of group of measure folders
  Type ‘modelkit rake’
Run all existing group of measures
  Use the provided python script

## Slide 18: New prototype system
Run specific existing group of measures
  Open cmd on one of group of measure folders
  Type ‘Modelkit rake’
Run all existing group of measures
  Use the provided python script
Results
  EnergyPlus Input files and hourly results
  Summary results

## Slide 19: Post-processing - Overview
Output from ModelKit E+
Data Format Transformation pre-SQL process
PostgreSQL process impact calculation + weights
DEER database impacts
QC workbooks
Notes: The results from Modelkit needs to be processed / transformed into DEER suitable formats
It takes several steps:
Data transformation for output of Modelkit
Apply PostgreSQL scripts to generate impact records
Final QC of the records

## Slide 20: Post-processing - PostgreSQL scripts revisited
A series of PostgreSQL queries, applied in sequence
Resulting table becomes the measure impact savings records for the DEER database.
Similar to previous MC3 post-processes, updated with some modifications
Simulation outputs (used to come from MASControl3)
DEER measure impacts
SQL Scripts do the following:
combine 1-story and 2-story data for Single Family
calculate kWh, therm and peak kW impacts (deltas)
apply HVAC weights / BldgType weights
round digits
(sim_annual.csv, sfm_annual.csv, current_msr_mat.csv, sim_hourly_wb.csv, sfm_hourly_wb.csv, etc..)
We need this format first..
Notes: Check the oven first.. See what type of inputs it takes in.
A series of PostgreSQL queries, applied in sequence (along with weights table informed by RASS),

## Slide 21: Post-processing - Python transformation before SQL
results-summary.csv
sim_annual.csv
sfm_annual.csv
current_msr_mat.csv
Output model IDFs, hourly consumptions, summary tables, etc.
sim_hourly_wb.csv
sfm_hourly_wb.csv
(EU tables as well, but work in progress)
Three BldgType specific scripts transform the data format of the Modelkit/E+ outputs to feed the postgreSQL scripts that produce the measure impacts.
Take individual hourly consumptions, rearrange into the 365x24 format sim_hourly / sfm_hourly
Take results-summary.csv rearrange into sim_annual / sfm_annual, apply correct normalizing units
Take all available info and create Measure-TechID relationship table (current_msr_mat)
Notes: Now we prepare what goes into the oven
3 BldgType specific scripts created to transform the data format of the Modelkit/E+ outputs such that it can be fed into the postgreSQL scripts, in order to produce the measure impacts.
SFM is different because there are two prototypes – single story and two story.

## Slide 22: GitHub
The remote repository can be accessed on sound-data/EnergyPlus (github.com)

## Slide 23: GitHub
Repository cloning example using GitHub Desktop (instructions available in the README.md file)

## Slide 24: GitHub
Repository cloning example using GitHub Desktop (instructions available in the README.md file)

## Slide 25: GitHub
Users bug fix and new measures addition
  Fork or create a new branch of the remote repository
  Make changes on your local repository
  Submit a pull request

## Slide 26: Updates to Calibration
Updated the foundation to crawlspace in the 1975 single family model for consistency with previous prototypes
Added two-dimensional finite difference heat transfer method (Kiva) for the foundation
We applied energy management system (EMS) to approximate the impact of duct loss for all building types
Natural ventilation added for all building types
Calibration parameters updated for all building types
Climate zone | Floor insulation | Duct Leakage ratio % | Shading control | Infiltration ACH
1 | NR | 20 | AlwaysOn | 0.35
2 | 2 | 14 | AlwaysOff | 0.35
3 | 6 | 20 | AlwaysOff | 0.35
4 | NR | 10 | AlwaysOn | 0.35
5 | 6 | 20 | AlwaysOff | 0.35
6 | NR | 20 | AlwaysOn | 0.50
7 | NR | 20 | AlwaysOn | 0.50
8 | NR | 25 | AlwaysOn | 0.35
9 | NR | 20 | AlwaysOn | 0.60
10 | NR | 15 | AlwaysOn | 0.35
11 | NR | 15 | AlwaysOn | 0.40
12 | NR | 15 | AlwaysOn | 0.35
13 | NR | 30 | AlwaysOn | 0.40
14 | NR | 15 | AlwaysOn | 0.35
15 | NR | 28 | AlwaysOn | 0.35
16 | NR | 15 | AlwaysOff | 0.35
Calibrated single family parameters
Notes: We added the crawlspace to our 1975 single family models to be consistent with previous DEER models and representative of old building stock.
We found the heat transfer through the ground has a significant impact on building energy consumption, which is especially true for residential buildings. We adopted a two-dimensional finite difference heat transfer method, called Kiva, that calculates ground heat transfer more accurately compared to traditional heat transfer methods in EnergyPlus.
We applied energy management system (EMS) to approximate the impact of duct loss. This is a user defined control that calculates the supply and return duct leakage heat loss and conduction heat transfer to the air handler zone based on multiple variables like the leakage ratio, duct area, duct R value, air flow rate, temperature, and humidity ratio etc. The Air flow rate and air properties within the duct and each zone are calculated at every time step of the simulation in EnergyPlus. The leakage ratio and duct characteristics were derived from the documentation of previous DEER versions.
we added natural ventilation into all our prototype models. In the previous DOE2/MC3 models, the natural ventilation occurred only between May 1st and September 30th with a minimum indoor temperature at which the ventilation stopped and a probability schedule (0.5) to indicate whether the occupants would open the window for natural ventilation or not. In our updated models, the natural ventilation is operating based on the indoor air temperature, the outdoor air temperature, and if the simulation timestep is in heating or cooling mode.
The calibration was performed separately for end uses of heating, cooling, and electric/gas base loads. We used modeled heating results from the prototype containing a forced air gas furnace in the calibration since over 60% of homes in California use this type of HVAC system. You can see the parameters that we calibrated in the table on the slide.

## Slide 27: Updates to Calibration Memo
Notes: Notice the heating energy consumption decreased across all climate zones between 2003 and 2019

## Slide 28: Updates to Calibration Memo
Notes: Notice cooling consumption did not increase across all climate zones between 2003 and 2019. It increased significantly in CZs 3, 5 and somewhat in CZ 16.

## Slide 29: Next Steps
Dec 2023 – Commercial prototypes will be added to the DEER Prototype system
Dec 2023 – Airflow Network will be added to the residential prototypes
Review and approve stakeholder updates to building prototype models and energy efficiency measures
Continue to work with CalBEM to update prototypes

## Slide 30: Questions

## Slide 31: DEER EnergyPlus Prototype System
DEER EnergyPlus Transition Webinar #3
Jennifer.McWilliams@dnv.com
510.390.5756